Purpose: hydrocarbon condensate drain pump

Quantity: 1 pc.

Type of pump: centrifugal or screw

| № | Наименование параметра (характеристики) | Размерность | Требования заказчика |
| --- | --- | --- | --- |
| 1 | ФУНКЦИОНАЛЬНЫЕ |
| 1.1 | Supply | m3/hour | 0,5…2,5 |
| 1.2 | Pressure | m | 40 |
| 1.3 | Inlet/outlet pressure (max.) (g) | kgf/cm2 | 0,01…0,03/0,4 |
| 1.4 | Cavitation reserve (max.) | m | - |
| 1.5 | For semi-submersible (submersible) pumps: |  |  |
| 1.5.1 | Immersion depth (distance from liquid surface to suction connection) | m | - |
| 2 | PUMPED MEDIUM |
| 2.1 | Name of pumped medium | Hydrocarbon condensate with hydrogen sulphide content up to 9% |
| 2.2 | Particulate matter content: |
| 2.2.1 | Volume concentration | % |  |
| 2.2.2 | Particle sizes (abrasive/non-abrasive) | mm | 0,25/0,25 |
| 2.3 | Temperature of working medium | 0С | +20 to +60 |
| 2.4 | Viscosity (kinematic) | cSt (mm2/s) |  |
| 2.5 | Density | kg/m3 | 600…700 |
| 3 | MATERIALS RESISTANT TO THE PUMPED MEDIUM |
|  | To be determined by the manufacturer/supplier |
| 4 | SHAFT SEAL |
| 4.1 | Single/double packing gland seal | To be determined by the manufacturer/supplier |
| 4.2 | Single/double mechanical seal |  |
| 5 | OPERATING (INSTALLATION) CONDITIONS |
| 5.1 | Климатическое исполнение |  | -53….+35 |
| 5.2 | Class of explosion hazard and fire zone of accommodation |  | В-1а |
| 5.3 | Need for cooling/heating medium supply | Yes/no | no |
| 6 | DRIVE/ACTUTATOR |
| 6.1 | Voltage, number of phases |  | 380 |
| 6.2 | Network frequency |  | 50 |
| 6.3 | Explosion protection version |  | Еxd |
| 6.4 | Rotational speed | ANY |
| 7 | ДОПОЛНИТЕЛЬНЫЕ ТРЕБОВАНИЯ |
| 7.1 | Spare parts for 2 years The pump must be supplied with flanges for PN 1.6 MPa, DN to be determined by the supplier/manufacturer, with flange flange flange flange face "B". Mating flanges, pads and fasteners are not required. The pump unit must withstand a temperature range of -53...+35 °C when not in operation. . |